## Slide 1
Heat Networks
Metering and Billing
Chris Smith
NMRO

## Slide 2: Regulations

## Slide 3: Scope 1
District Heat Networks
  Multiple buildings
  1 or more customers
Communal Heating
  1 building
  Multiple customers

## Slide 4: Scope 2
Apartment (domestic)
  Cooking facilities
  Sanitary facilities
  Used as living space
Multi use (non-domestic)
  Partitioned space
  Non-residential activity
  May be some shared services

## Slide 5: Scope 3
Heating via distributed
  hot water
  Steam
Cooling via distributed
  Chilled liquids
Hot water

## Slide 6: Duty to install meters or HCAs
For DH, block-level meters required for buildings with more than one final customer
Individual meters and temperature control devices must be installed unless it is not cost effective or technically feasible to do so
In buildings with more than one final customer, where individual meters are not viable, then heat cost allocators, TRVs and a hot water meter must be installed, where feasible

## Slide 7: Meter viability and meter accuracy
Meters must accurately measure, memorise and display consumption by a final customer.
Where the installed meter has been approved under the Measuring Instruments Directive (MID) and properly maintained the NMO will generally accept this as of appropriate quality

## Slide 8: New buildings and major renovations District Heat
Individual meters must be installed where a new DH connection is made to a newly constructed building, or where a building supplied by DH undergoes major renovation (that relate to the technical services of the building)
Major renovation is defined as costing greater than 25% of the value of the building, excluding land.

## Slide 9: New buildings and major renovations Communal
From 31 December 2016 individual meters must be installed where a to a newly constructed building, or where a building undergoes major renovation (that relate to the technical services of the building) where it is technically and economically feasible to do so.
Major renovation is defined as costing greater than 25% of the value of the building, excluding land.

## Slide 10: Billing
Where meters are fitted, if technically possible and economically justified bills and billing information must be accurate, based on actual consumption, and comply with Schedule 2
Heat Suppliers must not make a specific charge for the provision of a bill or billing information but reasonable costs may be passed on to final customers

## Slide 11: Timings
Came into force 18 December 2014
  DHN requirements from this date
Billing 30 December 2014
  DHNs and Communal
Notifications 31 December 2015
  Or completion of a project (i.e first customers) if after that date
For buildings with more than one final customer: viability tests (and any installation) by 31 December 2016
Bills at least annually and billing information at least twice per year

## Slide 12: Heat Supplier
Who is:
  Supplying heat to the Final Customer?
  Collecting payment?
  Buying fuel?
  Authority to fit meters?
Could be (case by case)
  Owner
  Operator/managing agent
  Service agent
  Other

## Slide 13: Feasibility
Technical and Economic
Return on investment in 10 years
Feasibility test does not apply to building level meters in multi-occupancy buildings on DHNs

## Slide 14: Notifications
31 December 2015
Notifications Template
Minimum of statutory information
UPRNs for Scotland
Bulk form
Incomplete forms will require follow up
  Email box: heatnotifications@nmo.gov.uk

## Slide 15: Approach to Enforcement

## Slide 16: Based on Intelligence and Risk
20%
20%
50%
Population/ Penetration
Likelihood
Low
High
Low
High
10%
Notes: 2 types of targeting shown each used in the same way:
Use identified risk to concentrate resources.
Lessen impact on compliant business.
Aid selection for initial activity

## Slide 17: Balanced Enforcement Model
Sanctioning
Support
Education
Push
Pull
Directed
Intervention
Non-directed
Intervention
Changing Behaviour

## Slide 18: Proportionate Actions
Informal Warning
Enforcement Undertaking
Compliance Notice
Non-compliance Penalty
Formal Caution
Court Action
Publicity
Severity

## Slide 19: Chris Smith National Measurement and Regulation Office Chris.Smith@nmro.gov.uk https://www.gov.uk/government/collections/national-measurement-office-enforcement-authority
?